## Slide 1: Model Predictive Control VS Deep Reinforcement Learning Control
Yangyang Fu
Texas A$M University
11/25/2020
Building HVAC System

## Slide 2: Agenda
Goal and Scope
Progresses

## Slide 3: Goal and Scope
Goal
  Compare the performance of MPC vs DRL/TL on building HVAC control
  Fault-tolerant control: MPC vs DRL
Scope
  Comparison:
    Single zone
    Multi-zones – 1 for now
  Fault tolerant control:
    Single zone
    Multi-zone – 1 for now

## Slide 4: System Description: Single Zone
Building HVAC – air side
  Single Zone
  Guideline 36 for air-side supervisory control
Control Testbed
  Inputs: air flow rate in kg/s

## Slide 5: MPC Development
Objective: minimize energy cost while satisfying zone thermal constraints
Control inputs
  Supply air flow rate – 5 level, same as DRL?
    Continuous or discrete: discrete for MPC
    CONTIOUS FOR fault-tolerant
MPC models
  Zone dynamics:
  Power Predictor:
Experiment
  Period: August
Training Data
  Excitation Experiment
    Period: July? Or August?

## Slide 6: DRL: OpenGym Environment
Github: https://github.com/YangyangFu/mpc-drl-tl.
Integrated environment for deep reinforcement learning using Modelica
  Jmodelica: simulate Modelica-based building energy system
  Opengym: interface for using Modelica models as DRL environment
  Pytorch: develop DRL algorithms
Build an openGym environment for single zone model
  Contained in a Docker file, which represents a virtual Ubuntu development environment
  Tested installation
  Future work:
    Reward policy – NU
    Test with DRL algorithm – q-learning example TAMU

## Slide 7: Next steps
TAMU:
  MPC development
  Help NU on integrating openGym environment with DRL
NU
  Test DRL in the openGym environment
  Develop fault-tolerant DRL